Physical Metallurgy Laboratory

Enquiry#MET/BSMT/2014/001	Date – 25/08/2014 Due on – 09-09.2014

Specification for automatic polishing machine – 1 No

Following are the equipment specifications for the automatic polishing machine proposed to be procured for the Physical Metallurgy Laboratory.

- Machine Size: The equipment size should not exceed 1000x500x750mm (h x w x l mm) in view of lab space management.

- Motor rating: Sufficient motor power for enabling variable low speed to high speed rpm in the sample loaded condition. Motor power could be either 1 or 1.5 HP / AC.

- RPM requirements: Variable speed 50 to 600 rpm.

- Polisher disc: The polisher disc size should be 10” and should have provision for easy dismounting and change to other standard supplied discs. Needs to have essential clamping arrangements for the abrasive sheets and/or magnetic sheets.

- Polisher Head: The machine should have independent head motor with a motor power of at least ¼ HP.

- Variable speed of the head to be 50 – 200 rpm

- Pneumatic pressure to be applied on the sample with the aid of a compressor. Should be capable of variable pressure of 1to 4 bars.

- Provision for interchangeable sample holder fixtures, to hold sample sizes of 1 ¼ “, 1 ½ “, and 2”

- Electronic controls with LCD display and digital timer.

- Power supply: 230V / 50Hz ( Single Phase + Neutral + Earth)

Note –

- Specification conformity certificate is required along with the competitive quotation.

- Quotations should be addressed to Prof.B.S. Murty, Head, Physical Metallurgy Laboratory, Department of Metallurgical and Materials Engineering, IIT Madras, Chennai – 600036.

Technical clarifications Pl Contact:Dr.B.S.Murty :9444077006 /

Mr.Parthiban :9940049780

- Quotations should mention in detail the separate prices for the basic equipment, accessories and the required consumables. Consumables and accessories that are necessary for a smooth regular daily operation for one year should be included in the quotation.

- Warranty should be covered for 1 year from the date of installation.

- Censico International Pvt. Ltd

Addess: 5 A Mahatma Gandhi Road 
                          Agra, Utter Pradesh
                          INDIA 282 002
            Mobile: +91-9837053777
            Phone: +91-562-2524777
           Email: info@censico.co.in
                    : censico@sancharnet.in

- Metal Power Analytical (I) Pvt. Ltd

| METAL POWER ANALYTICAL (I) PVT. LTD. |
| --- |
| Address: | B-48, Raj Industrial Complex, Military Road, Marol, Andheri (E), Maharashtra, India. Mumbai - 400 059 - INDIA |
| Tel: | +91-22-67830505 |
| Facsimile: | +91-22-29251373 |
| Mobile : | +91 919324665560 |
| Email: |  |
| Website : | www.spectrometersworld.com |

- Madras Metallurgical Services (P) Ltd.

P.B No.5553
24, Lalithapuram Street,
Royapettah, Chennai - 600 014.

Phone : +91 44 28133093, 28133903
Fax : +91 44 28131703 
Email : mmspl@vsnl.com | info@madrasmetallurgical.in

- Aimil Ltd.

Naimex House
A-8, Mohan Cooperative Industrial Estate,
Mathura Road, 
New Delhi - 110 044

Tel: 011-30810200
  Fax: 011-26950011
  Email: info@aimil.com

- Chennai Metco Pvt. Ltd.

SP100A, Ambattur Industrial Estate,
Chennai – 600 058, India
Phone: 91-44-2688 0737, 2688 0005, 
Fax: 91-44- 2688 0850
e-mail: mktg@chennaimetco.com

- Metatech Industries,
595, Shaniwar Peth, Gowaikar Complex,
Pune - 411030, India.
Tel. - +91 20 24450312, 24489295.
Fax - +91 20 24450530, 24450295.
e-mail: sales@metatechind.com, meta@metatechind.com

- S.R.Technologies Pvt. Ltd

No.100/3, 1st floor,

Block T, 3rd avenue, Anna nagar west

Chennai – 600040

Ph – 044 43012689

Fax – 044 43012689

Mobile – 9444033516

Email – srtech_metal@yahoo.co.in

www.srtechnologies.org.in

- Hitech India Equipments Pvt. Ltd

New No.26, Old No.91, 3rd street, karpagam avenue,

R.A.Puram, Chennai – 600028

Censico International Pvt. Ltd No: 5 A Mahatma Gandhi Road Agra, Utter Pradesh INDIA 282 002

METAL POWER ANALYTICAL (I) PVT. LTD. B-48, Raj Industrial Complex, Military Road, Marol, Andheri (E), Maharashtra, India. Mumbai - 400 059 - INDIA

Madras Metallurgical Services (P) Ltd. P.B No.5553 24, Lalithapuram Street, Royapettah, Chennai - 600 014.

Hitech India Equipments Pvt. Ltd New No.26, Old No.91, 3rd street, karpagam avenue, R.A.Puram, Chennai – 600028

S.R.Technologies Pvt. Ltd No.100/3, 1st floor, Block T, 3rd avenue, Anna nagar west Chennai – 600040

Metatech Industries, 595, Shaniwar Peth, Gowaikar Complex, Pune - 411030, India.

Chennai Metco Pvt. Ltd. SP100A, Ambattur Industrial Estate, Chennai – 600 058, India

Aimil Ltd.Naimex House A-8, Mohan Cooperative Industrial Estate, Mathura Road, New Delhi - 110 044

M/s. Comtech Computers, New No.39, Old No.18,Oil Monger Street, Royapettah, Chennai -600 014

M/s. OM Enterprises, 5, Patel Street, Venkateshwara Nagar, Ambattur, Chennai-600 053.

M/s. SBA Info Solutions Private Limited, No.52,(Old No.36) 48th Street, Ashok Nagar, Chennai – 600 083.

M/s. GAP Technologies, No.57, 1st Avenue, Indira Nagar, Adyar, Chennai-600 020.

Datalogics India Pvt. Ltd., 2nd floor, SIET College Avenue, 54, K.B. Dasan Road, Teynampet, Chennai- 600 018

Comtech Computers, New No.39, Old No.18,Oil Monger Street, Royapettah, Chennai -600 014

M/s. Dev Systems & Services, 25A, (New #56), Govindan Road, West Mambalam, Chennai - 33

M/s.SS Information Systems Pvt. Ltd., No1 /102, Periyar Pathai West, 100 Feet Road, Arumbakkam, Near Thirunagar Bus Stop, Chennai-106

M/s.Keystone Systems and Solutions Pvt Ltd. No. E 153, 7th Cross Street, Besant Nagar, Chennai 600 090.

M/sFujitsu India Pvt. Limited, No.31, Alraza Sernhill Apartment, 3rd Floor, T-2, 4th Main Road, Kasturbai Nagar,Adyar, Chennai – 600 020

Seven Hills Enterprises 162/42, South West Boag Road, T. Nagar, Chennai -17

M/s.Sri Balaji Enterprises, No.1, 1st Avenue, 7th Main Road Dhandeeswaram Nagar Velachery, Chennai – 600 042

| Sl # | PO # | Particulars | Value | Remarks |
| --- | --- | --- | --- | --- |
| 1 | DEPT/MET/201 | Fume Hood | 1,83,620.00 |  |
| 2 | DEPT/MET/202 | Wallworking Table-1 no/ WallStorage Cupboard -5 no | 1,89,781.00 |  |
| 3 | DEPT/MET/203 | Wallworking Table-1 no/ WallStorage Cupboard -1 no | 1,25,661.00 |  |
| 4 | DEPT/MET/205 | Wallworking Table-1 no/ Revolving Stool - 9 no | 1,28,180.00 |  |
| 5 | DEPT/MET/009 | GAS | 1,84,616.75 | Not claimed |
| 6 | MET/HOD/2013/201 | Civil/Electrical | 57,40,747.00 | POValue71,75,935/- |
|  |  |  | 65,52,605.75 |  |
|  |  | To be ammended | 27,31,306.00 | Not Claimed |

Project # ACC/13-14/153/TEM/FDSAN

| Sl # | PO # | Particulars |  | Value |
| --- | --- | --- | --- | --- |
| 1 | MET/2013/1023/SPLX | UPS | M/s Numeric | 6,55,147.00 |
| 2 | MET/2013/1061/SPLX | Vaccum Cleaner | M/s The Ultimate | 35,924.00 |
| 3 | `MET/2014/1007/SPLX | Door Acess system | M/s Dhonadhi | 43,758.00 |
| 4 | `MET/2014/1001/SPLX | Door Acess system | M/s Dhonadhi | 1,96,685.00 |
| 5 | DEPT/MET/2014/1022/SPLX | Curtain | M/s Sri venkateswara | 1,97,678.00 |
| 6 | DEPT/MET/2014/1024/SPLX | Curtain | M/s Sri venkateswara | 1,77,322.71 |
| 7 | DEPT/MET/2014/1026/SPLX | CS channel | M/s Sri venkateswara | 44,884.00 |
|  | 13,51,398.71 |

Dear Mr. Prakash,

I am planing to buy Sony laptop Model: SVF14N16SNS. However, it is not in the rate contract.
Could you please call for quotation with the following specification.

CPU: Intel® Core™ i5 Processor (1.60 GHz)
OS: Windows 8
Display : 14 (35.6 cm); touch screen
Memory : 4GB
Hybrid HDD : 1 TB
Flip and convert into tablet
Weight: <2 kg. (including battery)


With thanks and regards
Dr. Sabita

Iwould like to purchase the following items from department funds.

Item ID: DSK5
HP1 HPEliteDesk 800G1 Rs. 49725.00

Item ID: PLS8

HP HP LJ Pro M1536dnf MFP Printer:IN Rs. 22550

Please see the details in the attached pdf. I have highlighted the items in the rate contract.

Thanks.

With best regards,
Manas Mukherjee

Sarkar