Construction of composting plant at Vichoor village- Activity 4

| 4 | Finishing including flooring, plumbing & electrical work | Unit | Qty |
| --- | --- | --- | --- |
| 4.a | Providing and fixing M.S. grills of required pattern in frames of windows etc. with M.S. flats, square or round bars etc. including priming coat with approved steel primer all complete. | kg | 2750 |
| 4.b | 12 mm cement plaster of mix : 1:4 (1 cement: 4 fine sand). | sqm | 363 |
| 4.c | Cement concrete flooring 1:2:4 (1 cement : 2 coarse sand : 4 graded stone aggregate) finished with a floating coat of neat cement, including cement slurry, but excluding the cost of nosing of steps etc. complete. 40 mm thick with 20 mm nominal size stone aggregate | sqm | 200 |
| 4.d | Finishing walls with water proofing cement paint of required shade : New work (Two or more coats applied @ 3.84 kg/10 sqm over a coat of cement primer) | sqm | 363 |
| 4.e | Finishing with Epoxy paint (two or more coats) at all locations prepared and applied as per manufacturer’s specifications including appropriate priming coat, preparation of surface, etc. complete. On steel work | sqm | 140 |
| 4.f | Providing and fixing soil, waste and vent pipes : UPVC Pipe 4kg/sqcm including all fittings. |  |  |
| i | 75mm dia | Rm | 50 |
| ii | 110 mm dia | Rm | 25 |
| 4.g | Providing and fixing Chlorinated Polyvinyl Chloride (CPVC) pipes, having thermal stability for hot & cold water supply, including all CPVC plain & brass threaded fittings, including fixing the pipe with clamps at 1.00 m spacing. This includes jointing of pipes & fittings with one step CPVC solvent cement and testing of joints complete as per direction of Engineer in Charge. 25 mm nominal outer dia Pipes |  |  |
| i | 25 mm nominal outer dia Pipes | Rm | 50 |
| ii | 40 mm nominal outer dia Pipes | Rm | 25 |
| 4.g | Supplying at site : R.C.C. Standards post/ struts/rails/ pales of mix 1:1.5:3 (1 cement : 1.5 coarse sand : 3 graded stone aggregate 12.5 mm nominal size) with wooden plugs or 6mm bar nibs wherever required as per direction of Engineer-incharge (cost of earth works in excavation, concrete works in foundation to be paid separately). | cum | 1.1 |
| 4.h | Provide well rings for composting plant with equal distance at 1500mm | Nos | 8 |