SPECIFICATION FOR GAS LINING WORK

| S.no | Product Description | Qty | Unit Price in Rupees | Total Price in Rupees |
| --- | --- | --- | --- | --- |
| 1. | Five Cylinder Manifold System for ICP-MS for Argon Gas 5 x 1 Cylinder Manifold system to connect Five cylinders with single outlet consists High Pressure Shut-off valve with Built-in the holder, provision for direct pigtail and regulator Teflon braided SS pigtail 1 meter length – 5 Nos. Non-Return Valve – 5 Nos MS Frame to hold the Manifold – 1 No. (Cylinder Regulator not included) | 1set |  |  |
| 2. | Single cylinder SS Manifold System for Mayura GC (N2/H2/Air) and ICP-MS (Helium/ Methane) Single Cylinder Manifold system to connect single cylinder with single outlet consists of SS Block to Hold Pigtail & Regulator Teflon braided SS pigtail 1 meter length – 1 Nos. MS Frame to hold the Manifold – 1 No. (Cylinder Regulator not included) | 5sets |  |  |
| 3. | Single cylinder SS Manifold System for Purging Line (Fume cupboard & other rooms) (N2/H2/Ar/Air/oxygen/CO2 and spare) Single Cylinder Manifold system to connect single cylinder with single outlet consists of SS Block to Hold Pigtail & Regulator Teflon braided SS pigtail 1 meter length – 1 Nos. MS Frame to hold the Manifold – 1 No. (Cylinder Regulator not included) | 7set |  |  |

| 4. | Gas Change over Unit Supplied with 1/4” one Inlet & 1/8” Nine outlet ¼” One outlet for Nitrogen With Shut-off valve. | 1set |  |  |
| --- | --- | --- | --- | --- |
| 5. | Gas Change over Unit Supplied with 1/4” one Inlet & 1/8” Seven Outlet ¼” One outlet for Argon With Shut-off valve. | 1set |  |  |
| 6. | Gas Change over Unit Supplied with 1/4” one Inlet & 1/8” Eight Outlet for Spare Line with Shut-off valve. | 1set |  |  |
| 7. | Gas Change over Unit Supplied with 1/4” one Inlet & 1/8” One Outlet and ¼” one outlet for Oxygen with Shut-off valve. | 1set |  |  |
| 8. | Gas Change over Unit Supplied with 1/8” one Inlet & 1/8” Three Outlet for Hydrogen/Air/Oxygen With Shut-off valve. | 3set |  |  |
| 9. | Control Unit for Nitrogen Supplied with 1/8” Inlet & 1/8” Outlet, Consists of Pressure Gauge (0-10Kg/cm2), Pressure Regulator & Shut-off valve. | 9nos |  |  |
| 10. | Control Unit for Argon Supplied with 1/8” Inlet & 1/8” Outlet, Consists of Pressure Gauge (0-10Kg/cm2), Pressure Regulator & Shut-off valve. | 7nos |  |  |
| 11. | Control Unit for Spares Line Supplied with 1/8” Inlet & 1/8” Outlet, Consists of Pressure Gauge (0-10Kg/cm2), Pressure Regulator & Shut-off valve. | 8nos |  |  |
| 12. | Control Unit for Hydrogen/ Air /Oxygen Supplied with 1/8” Inlet & 1/8” Outlet, Consists of Pressure Gauge (0-10Kg/cm2), Pressure Regulator & Shut-off valve. | 3nos |  |  |
| 13. | Control Unit for CO2/Oxygen Nitrogen/Argon Supplied with 1/4” Inlet & 1/4” Outlet, Consists of Pressure Gauge (0-10Kg/cm2), Pressure Regulator & Shut-off valve. | 4nos |  |  |
| 14. | Cylinder Holding Chain with bracket | 25nos |  |  |
| 15. | Heater for CO2 | 1no |  |  |
| 16. | 1/8" SS 316 Flexible high grade Tubing with color coded sleeves (Billing will be done as per usage) | 1000 Mtrs |  |  |
| 17. | 1/4" SS 316 Tubing - Estimated Requirement (Billing will be done as per usage) | 100 Mtrs |  |  |
| 18. | Aluminum Casing & Capping (Kindly mention the exact requirement in meter while ordering) | 250 Mtrs |  |  |
| 19. | Flash Back Arrestor for Hydrogen | 2nos |  |  |
| 20. | Assorted Fittings | 1set |  |  |
| 21. | Double Stage Double Gauge SS Regulator with SS Diaphragm. Supplied with suitable end fittings (for Nitrogen-2nos, Hydrogen-2nos, CO2-1no, Zero Air-2nos, Argon-2nos, Oxygen-1no, Spare -2nos) | 14nos |  |  |