Load Cell Specifications

A 6-axis load cell of following specification is required. If the values are different please provide the closest product and mention the value of the parameter in the third column. This should be a complete system including software and data acquisition. Alternately, vendor can provide necessary electronics to interface the load cell with labview (available with user). The load cell should be calibrated and ready to use and no calibration will be performed at user end.

| Specification | Range | Actual value for product |
| --- | --- | --- |
|  | 0 – 50 |  |
|  | 0 – 100 |  |
|  | ≈2.5 |  |
|  | ≈2.5 |  |
| Weight (kg) | ≈ 0.5 |  |
| Height (mm) | ≈ 50 |  |
| Diameter (mm) | ≈ 100 |  |
| Resolution | : 0.02N |  |
|  | : 0.001 Nm |  |
| Accuracy | Nonlinearity : <0.1% Rated output |  |
|  | Hysteresis : <0.1% Rated output |  |
|  | Repeatability : <0.1% Rated output |  |
| Safe Overload | >150% of Rated output in all axis of measurement |  |