Vacuum Chamber Specifications

A room of approximate dimension 11 ft x 10 ft x 8ft need to be converted to a low pressure chamber by using a vacuum pump. The pressure (range: 1 bar-0.008 bar) in the room should be adjustable or set using a control panel. The time to reach the lowest pressure of .008 bar should be less than 2 hours. A general sealing of the room will be done by IIT, however any minor leakage/gaps should be fixed by the vendor. The room requires a door for entry of personnel and also a window to view. In addition, there should be provision for taking cables (signal/electrical).

Specifications for the room and the door are given below.

| Room dimension | (Appx)11 ftx10 ftx8 ft |
| --- | --- |
| Required Vacuum level | ~1/100 atmosphere (~10 milli Bar) |
| Pressure control method | Using on off solenoid valve with less than 1-2%fluctuation in pressure level. (If other methods are available kindly mention) |
| Temperature control | Not Required |
| Door specifications | Vacuum chamber Door Size of door: 1500 x 700 mm Material: Stainless steel Window size on the door: 400 x 600 mm Window material: 12 mm thick acrylic |
| Air tight glands to tap power and signal wires |  |