|  | Department of Aerospace Engineering Indian Institute of Technology Madras Chennai – 600 036, India |
| --- | --- |

Dr. A. Sameen

PROJECT COORDINATOR

Ref : No. ASE/ASAM / ISRO / CLUSTER MGT / 2015/      		 		DATE: 14.05.2015

Dear Sir,							       			   Due date :  05.06.2015

- Quotations are invited in duplicate for the various items shown below/overleaf/enclosed list.

- The quotations are to be in two parts as Technical Offer and as Commercial offer:

The two parts of the offer are to be clearly marked on the envelopes. The two parts of the offer in separate envelopes must be enclosed in the one bigger envelope duly sealed and super scribed with reference number and due date and must be addressed to the undersigned so as to reach him on or before the due date stipulated above.

- Fax and Email quotation are not acceptable.

- Quotations should be valid for 60 days from the due date and period of delivery required, warranty terms etc. should also be clearly indicated. A minimum of one year warranty is required from the date of commissioning.

- Imported supplies should be quoted for CIF Madras.

- Local firms to quote for free delivery to this Institute. If quoted for Ex-Godown delivery charges be indicated separately.

- Relevant literature pertaining to the items quoted with full specifications (and drawing, if any) should be sent along with the Quotations, wherever applicable. Samples / machine/ equipment if called for should be submitted / demonstrated at free of charges, and collected back at the supplier’s expenses. Compliancy certificate is to be provided indicating conformity to the technical specifications

- Sales Tax/General Taxes/ED if applicable and such other taxes legally leviable and intended to be claimed should be distinctly shown along with the price quoted. If this is not indicated no such claim will be admitted at any stage. The taxes leviable should take into consideration that we are entitled to have concessional Sales Tax applicable to Non-Government Educational Institutions run with no profit motive for which a concession is given. Sales Tax Certificate will be issued at the time of final settlement of the bill.

- Goods should be supplied carriage paid and insured.

- Goods shall not be supplied without an official supply order.

- If the item is under DGS&D Rate contract No. and the price must be mentioned.  It may also please be indicated whether the supply can be made direct to us at the Rate contract price (Please note that we are not Direct Demanding Officers).  If so please send copy of the RC.

- The Guarantee period of the item may be indicated clearly.

- In case of LC. Payment, 90% of the payment will be made after completion of the supply. The balance 10% of the payment will be made after satisfactory installation of the equipment.

- IIT Madras is exempt from payment of Excise Duty and is eligible for concessional rate of custom duty. Necessary certificate will be issued on demand. IIT Madras will make necessary arrangements for the clearance of imported goods at the Airport/Seaport. Hence the price should not include the above charges.

- Acceptance and Rejection:- I.I.T. Madras has the right to accept the whole or any part of the Tender or portion of the quantity offered or reject it in  full without assigning any reason.

Yours faithfully

-sd-

Project coordinator

Items required: CLUSTER MANAGEMENT & MONITORING SOFTWARE as per specifications enclosed.

---------------------------------------------------------------------------------------------------------------------------------------------------

Phone Nos.:  (044) 2257 5000 / 4013 FAX: (044) 2257 4002, E-mail: sameen@ae.iitm.ac.in

Specification for Cluster Management & Monitoring Software

| S.NO |  | Requirement Description |
| --- | --- | --- |
| 1 | Master Node: Quantity 1 |
|  | CPU | Dual CPU - E5-2650 V3 2.4GHz 10 Core 25 MB Cache |
|  | Chipset | Intel C610 Chipset |
|  | Memory | 64GB ( 4x 16GB) DDR4 Reg. ECC 2133 MHz expandable to 1024GB |
|  | HDD | 2x 2 TB hot-swap SATA Enterprise class 7.2K rpm with support for 4 HDD bays |
|  | RAID | Raid controller with RAID 1. |
|  | Network | At least 2* 1G Ports , 1 x dedicated management LAN port for IPMI 2.0 compatible & 1x Dual Port QDR 40Gbps card with infiniband cables |
|  | Slot | At least 1x PCI-E 3.0 x16 slots & at least 1x PCI-E 3.0 x8 slots |
|  | Interface | 5 x USB 3.0 / 1 * USB 2.0 |
|  | Power Supply | 450W Redundant Platinum Level (94%) Power Supplies |
|  | Form Factor | 1U/2U Rack Server with rack mount rail kit |
|  | Warranty | Warranty: 3 years on-site comprehensive warranty |
| 2 | Compute Node: Quantity 2 |
|  | CPU | Dual CPU - E5-2650 V3 2.4GHz 10 Core 25 MB Cache |
|  | Chipset | Intel C610 Chipset |
|  | Memory | 64GB ( 4x 16GB) DDR4 Reg. ECC 2133 MHz expandable to 386 GB |
|  | HDD | 1x 1TB hot-swap SATA Enterprise class 7.2K rpm with support for at least 4 HDD bays |
|  | Network | 2x Gigabit Ethernet Port ,1 x dedicated management LAN port for IPMI 2.0 compatible & 1x Dual Port QDR 40Gbps card with infiniband cables |
|  | Interface | Interfaces :2 x USB 3.0 |
|  | Power Supply | Redundant High-efficiency Platinum Level Power Supply |
|  | Form Factor | Dense form factor with 1600W Redundant Platinum Level (94%) Power Supplies / Redunant fans |
|  | Warranty | Warranty: 3 years on-site comprehensive |
| 3 | Switch | 40Gbps Infiniband Switch with at least 16 Ports – 1no. with 3 years Onsite Warranty |
| 4 |  | Job Scheduler Software: Open Source Job Scheduler like Torque/SGE or equivalent. |

Cont….

- 2 -

|  |  | Cluster Management & Monitoring Software: |
| --- | --- | --- |
|  |  | GUI based Cluster Management (Add, Modify, Delete Compute Nodes) |
|  |  | Fully automated system provisioning |
|  |  | GUI Interface for Monitoring overall health of cluster |
|  |  | GUI Interface for cluster Provisioning and Management |
|  |  | Profile based compute node, storage node provisioning |
|  |  | Managed Services from cluster tool (DNS, DHCP, NIS etc.) |
|  |  | Must support various flavor of Linux OS RedHat and CentOS |
|  |  | Must support configuring InfiniBand & GigE network ports of compute nodes, port bonding etc. |
|  |  | Configuration Automation (installation of Application in compute node through Cluster Management Tool) |
|  |  | Add/Delete/Disable users, group |
|  |  | Monitor cluster nodes status including drill-down of monitored events |
|  |  | User friendly GUI Web based portal for Job submission. |
|  |  | Secure and Authorized access to cluster resources. |
|  |  | Support for integration with LDAP / AD for user authentication. |
|  |  | Application integration with the portal. |
|  |  | Quoted Job Scheduler integration with the GUI portal. |
|  |  | Cluster health reporting |
|  |  | GUI display of Cluster Hardware & Software configuration |
|  |  | OEM (Manufactures) should have at least 5 HPC installations in latest listing of Top 500 supercomputer list. |
|  |  | The bidder (System Integrator) should submit the authorization letter from the OEM’s. OEM should authourize only one bidder & the bidder also bid only one OEM product. |
|  |  | The bidder (System Integrator) or OEM should have Technical expertise in implementing cluster which includes installation configuration, maintenance and customization as per requirement. |
|  |  | Master/Head Node, Compute Node and Cluster Management and monitoring software should be from the same OEM. |