Technical Specification for UV-Vis Spectrometer

| Wavelength range | 190 -1100 nm |
| --- | --- |
| Bandwidth | Variable (0.5 – 5 nm) |
| Monochromator | Sealed |
| Source | Deuterium & Tungsten |
| Wavelength accuracy | ( 0.1 nm |
| Wavelength reproducibility | ( 0.1 nm |
| Photometric system | Double beam |
| Photometric range | ( 4 A |
| Photometric accuracy | ( 0.004 A |
| Photometric noise | < 0.00005 A |
| Photometric drift | < 0.0005 A/hour |
| Baseline flatness | ( 0.001 A |
| Scan speed | Variable |
| Software | Appropriate software for spectral acquisition and manipulation, should be user friendly |
| Size and Weight | Should be a table top unit, < 35 kg weight |

Power Supply			: 230 V/50 Hz

Spare and accessories 		: Include all necessary spare and accessories for two years of

operation.

Computer			: The necessary computer specification must be provided.

Software must be Windows 7 or higher version compatible.

Connectivity with the computer through USB port.

Warranty Period		: Minimum Two years from the date of installation.

(Essential requirement).