Technical specification for UV-VIS spectrometer:

| Wavelength range | 190 nm- 1100 nm |
| --- | --- |
| Bandwidth | 1 nm |
| Monochromator | Sealed |
| Wavelength accuracy | ± 0.1 nm |
| Photometric system | Double beam |
| Wavelength reproducibility | ± 0.05 nm |
| Photometric accuracy | ± 0.001 A |
| Photometric range | -6 to 6 Abs. |
| Photometric stability | < 0.00015 A/hour |
| Baseline flatness | ± 0.001 A |
| Scan speed | Variable |
| Software | Appropriate software for spectral acquisition and manipulation |
| Size and weight | Table top unit |

Power requirements – 230V/ 50 Hz

Spares and accessories for two years of operation

Warranty Period: Minimum TWO years from date of installation (mandatory).

Computer: Desk top computer will be procured by us based on your specification.