High Speed Camera

CMOS based Monochrome High Speed Camera with capability to capture at least 2,000 frames per second at 1MP resolution and 160,000 frames per second at reduced resolutions. The camera should be capable of recording blur free images with exposures of 5µs or less.

| Specifications of High Speed Camera |
| --- |
| SL No | Parameter | Specification |
| 1 | Resolution | 1.3 MP or better |
| 2 | Sensor | CMOS Monochrome with pixel size of ≥10µm. |
| 3 | Frame rate | ≥2,000 fps at 1.3 Mega pixels ≥4,000 fps at 1024 x 512 pixels ≥10,000 fps at 640 x 240 pixels ≥160,000 fps at lower resolutions |
| 4 | High Speed RAM | 32GB or greater |
| 5 | Shutter Speed | ≤ 5µs |
| 6 | Dynamic Range | 12-bit Monochrome |
| 7 | Region of interest | Selectable in steps of ~ 128 x 8 pixels |
| 8 | Trigger Modes | Start, end, center, manual, random |
| 10 | ISO 12232 Ssat sensitivity | At least ISO 10,000 (Mono) |
| 11 | Trigger Options | Trigger from camera control software and external trigger using BNCs |
| 12 | Control Software | The camera control software should display the record parameters like frame rate, resolution, record duration, trigger mode, shutter speed etc before recording. The camera control software should be capable to let the user review/ crop recorded video before saving. The camera control software should have basic image processing tools like brightness, contrast, gamma. The camera control software should assist the user in focusing of image. The user should be able to correct lens distortion effects. |
| 13 | Operating temperature | At least up to 40 degree Celsius |
| 14 | Weight | ≤ 2 KG |
| 15 | Power Requirements | 100 to 240V, 50 to 60Hz AC |